## Slide 1: Semester Project Robotic assembly of large-scale timber structures
Ibois
Genilloud Florian
01.09.2020
École Polytechnique Fédérale de Lausanne (EPFL)
Ibois
Assistant: Nicolas Rogeau
Professor: Pr. Yves Weinand
Ecole Polytechnique Fédérale de Lausanne

## Slide 2: Content
State of Art
Depth Camera
Camera + Laser
Other methods
Conclusion
Ecole Polytechnique Fédérale de Lausanne
Ibois

## Slide 3: State of art
Use of a camera without autofocus (C270)
Need to find a way to improve the calibration
Must be the most precise for the insertion vector
Ibois

## Slide 4: Depth Camera
Intel RealSense D435 RGB-D
Price: ~200CHF
Range : optimal at 50cm
Precision: 1-5mm, 1-3°
Calibration using openCV tools
Ref: Highly accessible platform technologies for vision‑guided, closed‑loop robotic assembly of unitized enclosure systems, Daniel Tish, Nathan King, Nicholas Cote
Ibois
Ecole Polytechnique Fédérale de Lausanne
Robotic assembly of large-scale timber structures

## Slide 5: Depth Camera
Intel RealSense D435 RGB-D
Ibois
Ecole Polytechnique Fédérale de Lausanne
Robotic assembly of large-scale timber structures

## Slide 6: Depth Camera
Intel RealSense D435 RGB-D
Ref: Highly accessible platform technologies for vision‑guided, closed‑loop robotic assembly of unitized enclosure systems, Daniel Tish, Nathan King, Nicholas Cote
Ibois
Ecole Polytechnique Fédérale de Lausanne
Robotic assembly of large-scale timber structures
Pros | Cons
Cheap | Error increase with the range
Precise enough for the task | Hard to calibrate (tool center- camera position)
Can segmentize the image | Need background on the image

## Slide 7: Point-laser
HTPOW KGL-850 point Laser green 50mw  40 CHF
  (-) can be used less than 5 min in a row
  (-) Need to change the battery each time it’s out of energy
  (+) Relatively powerful
  (+) As a good linearity
    https://www.laserfr.com/KGL-850-laser-vert-50mw-point.html
Laser LT 104 point laser red 50mw  15 CHF
  (+) High capacity battery
  (+) Battery is rechargeable
  (+) Good heat dissipation
    https://www.laserpointeur.com/c-40_77_78-p-10085.html
Other ones exist
Ibois

## Slide 8: Point-laser for distance
Price : 10-40CHF
Range: 10cm-1m
Precision: ~1mm
Calibration: Use Paper, Ruler, and Pixel Ref: ferenc-nemeth/opencv-laser-rangefinder
Ibois
Ecole Polytechnique Fédérale de Lausanne
Robotic assembly of large-scale timber structures

## Slide 9: Point-laser for the distance
https://www.youtube.com/watch?v=bvDV_c-mpdM&ab_channel=Ferenc
Ibois

## Slide 10: Point-laser for distance
Ref: https://www.instructables.com/id/Making-Rangefinder-Using-a-Laser-and-a-Camera/
Ibois
Ecole Polytechnique Fédérale de Lausanne
Robotic assembly of large-scale timber structures
Pros | Cons
Cheap | Error increase with the range
Precise enough for the task | Need to manually activate the laser when need it
Relatively easy to calibrate | The laser needs to be out of the arUco

## Slide 11: Point-laser for orientation
Price : 20-80CHF
Range: 10cm-1m
Precision: ~1mm, angle not determ.
Calibration as before
Ibois
Ecole Polytechnique Fédérale de Lausanne
Robotic assembly of large-scale timber structures

## Slide 12: How to know the orientation?
angle desired(β) = 90°- α
α
a
b
a · b = ||a|| ||b|| cos(α)
Different solutions to find β :
Use Edge detection
Use arUco coordinate
β
Other ways to compute β ?
Ibois

## Slide 13: Point-laser for orientation
Ibois
Ecole Polytechnique Fédérale de Lausanne
Robotic assembly of large-scale timber structures
Pros | Cons
Add precision on the angle | Error increase with the range
Relatively easy to calibrate | Need to manually activate the laser when need it
Able to compare Laser and arUco precision to decide which is the best | Need to be sure that the points are well defined

## Slide 14: Orientation without arUco
Change the arUco by a black line parallel with the border.
Use Gaussian filters for Edge detection
The one with the highest convolution pick gives the angle
laser to compute distance.
Ibois
Ecole Polytechnique Fédérale de Lausanne
Robotic assembly of large-scale timber structures

## Slide 15: Other methods
Keep the system as is
  Find a way to improve the calibration
  Then, if needed, add the laser
  Maybe change the code for live tracking
Use some Machine learning algorithm
  Use the robot and camera to get data
  Work on the data to find a model which can predict the position (Bayesian Filter)
Change the camera for a better one
Ibois

## Slide 16
Slide From Nicolas Rogeau
Ibois

## Slide 17: Questions ?
Thank you for you attention
Ibois
Ecole Polytechnique Fédérale de Lausanne
Robotic assembly of large-scale timber structures